This master should be used by designers working on Port of Portland construction projects and by designers working for PDX tenants (“Tenants”).  Usage notes highlight a few specific editing choices, however the entire section should be evaluated and edited to fit specific project needs.

This section should be used for airfield work at general aviation airports.

SECTION 013513 - AIRPORT SECURITY, SAFETY, AND OPERATING REGULATIONS

GENERAL

AIRFIELD SECURITY (GENERAL AVIATION)

In area of work activities, the Contractor shall maintain security against unauthorized access to the airfield area through the security gate.

Access to the work site in the airfield environment shall be through the Project Security gate as shown on the drawings.

Temporary fence replacement panels and gates shall provide the same level of security and protection against unauthorized access as the adjacent security fence.  Temporary fences may utilize undamaged salvaged fence materials.  Fence materials need not be galvanized, and posts may be driven.  Height of fence or gate woven-wire fabric shall match height of adjacent security fence fabric.  Construct replaceable panels, used in lieu of gates or temporary fencing, so that they provide protection against unauthorized access equal to that of the gates and temporary fencing specified herein.  Use of such panels is subject to the Port’s approval.

All equipment and vehicles shall be positioned a minimum of 10 feet away from either side of the perimeter security fence.

REGULATIONS FOR CONTRACTORS

To the extent that any rules and regulations contained in this section conflict with the rules and regulations now or hereafter adopted by the Port, the rules and regulations adopted by the Port shall control.

The regulations contained in this section and the regulations adopted by the Port are subject to change at any time without notice.  Copies of current rules and regulations may be obtained during the Port’s normal business hours at the General Aviation Airport Manager’s office in the Portland International Airport terminal building or the Assistant Manager’s office at Hillsboro Airport.

DEFINITIONS

Airfield environment - areas restricted to public access on the airfield.

Airport Operations Manager - Operations Manager responsible for coordinating all airfield construction/maintenance projects.

Apron - All areas and facilities used for aircraft support and servicing operations.  It includes the following subcomponents:

Aircraft parking positions - Used for parking aircraft to enplane and deplane passengers, load or unload cargo.

Taxi lanes - Reserved to provide taxiing aircraft with access to and from parking positions.

Service/Fire lanes - Identified routes on apron designated for aircraft ground service vehicles and fire equipment.

Equipment - every self-propelled vehicle not capable of being used on a street or roadway.

Movement area - the area of an airport open and used by aircraft for taxiing, takeoff, and landing.  Aircraft or vehicle operations within this area require an air traffic control clearance from the Control Tower.

Ramp - paved areas adjacent to runways and taxiways where aircraft are positioned for servicing or parking.

Security gate - any controlled, securable opening in the security fence.

Vehicle - every licensed, self-propelled vehicle capable of being used on a street or roadway.

Work area - limits of work established by a perimeter boundary shown on the drawings or otherwise designated by the Port.

TRAINING INFORMATION

All Contractor personnel who will be working within the airfield environment shall attend an airfield orientation/driver training, escort driver or flagger training class conducted by the Airport Operations Manager as part of the requirements to obtain authorization to operate on the airfield.

The Contractor shall contact the Airport Operations Manager to schedule training classes for all Contractor’s and subcontractor’s personnel.

The Contractor shall provide a minimum of 48 hours’ advance notice to schedule training class requests.

No training classes will be available on Saturdays or Sundays.

Training classes will be limited to 25 people, maximum, per class.  Multiple classes may be arranged for the same day.

The approximate duration of the training classes are as follows:

Airfield Orientation/Driver			1 hour

Escort Driver			1/2 hour

Flagger			1/2 hour

DRIVING REGULATIONS

The purpose of these regulations is to maintain the safety of vehicle operations in the airfield environment.

Enforcement of these regulations will be by the Port, Police, or Airport Operations Staff.

Violations of the regulations may be cause for the project to be stopped and project safety procedures evaluated.  The Port will decide if and when work will continue.

The driving regulations are as follows:

Yield the right-of-way to moving aircraft, whether under tow or their own power, and pedestrians.

Within the airfield environment, equipment, vehicle, and personnel travel outside the work area is restricted to the route(s) shown on the drawings.

Obey stop signs and markings.

Yield right-of-way to emergency vehicles displaying rotating beacons (other than amber) and/or using sirens and other audible emergency signals.

Observe the posted speed limits.

Regardless of a posted speed limit, a lower speed may be required in order to account for congestion, reduced visibility, slippery surfaces, or other hazardous condition.  No vehicle shall be driven in a manner that endangers persons or property.

The speed limit of off-ramp service roads (perimeter road) is 25 MPH or as posted.

Motor vehicles shall be equipped with omni-directional amber flashing light, head lights, tail lights, and flashers that shall be used between sunset and sunrise or when visibility is low.

Non-motorized equipment shall have reflective devices displayed on the front, back, and sides.

Operators shall have a current and valid state driver’s license on their person.

Do not leave the engine running on an unattended vehicle.

Vehicles operating in aircraft movement areas require the following:

Escort provided by Port or designated personnel.

Omni-directional amber flashing light, clearly visible from all angles.

Radio equipped with Ground Control Frequency

Park unattended vehicles clear of service and perimeter roads.

Vehicles within the airfield environment shall display company identification markings on both sides of vehicle.

Loads being carried shall be contained by sufficient means to assure no loss of any portion of the load.

When outside the work area, all Contractor personnel, vehicle, and equipment movement within the airfield environment shall be under control of the Contractor’s personnel authorized to perform escort responsibilities with the Contractor’s approved escort vehicle(s).

The Contractor escort vehicle(s) shall be equipped with an amber flashing light mounted on the roof of the cab.  The escort vehicle(s) shall have signs mounted on the front and rear of the vehicle consisting of a black background and yellow lettering containing Contractor’s name and the words “ESCORT ONLY.”  Signs shall be readable from a distance of 300 feet.  Escort vehicle(s) shall have an FAA orange and white checked flag, 3 feet by 3 feet minimum, attached to a pole mounted on the rear bumper, and visible from 300 feet at all angles.

The escort vehicle driver shall serve as liaison and shall be responsible for transporting workers to and from the work area.

Personnel and vehicles authorized in the airfield environment shall remain with the escort vehicle(s) while traveling to and from the work area.

Multiple vehicles may be escorted in convoy formation.  Convoy vehicles shall travel in close formation, and the escort vehicle driver shall control speed to maintain safety.  Convoys shall consist of no more than three vehicles plus the escort vehicle.

All supervisory and survey personnel vehicles which operate unescorted within the airfield environment but outside the work area shall have a company vehicle with an amber flashing light mounted on the roof of the cab and identifying markings, visible from 300 feet, mounted on both sides of the vehicle.

All Contractor’s activities within aircraft movement areas shall have an additional escort provided by the Port or designated personnel.

OTHER SECURITY AND SAFETY REGULATIONS

No smoking will be allowed within the airfield environment except as designated by the Port.

Earplugs shall be furnished by the Contractor for personnel in air operation areas to eliminate the chance of ear damage.

While driving or working in the airfield environment, there shall be no devices in or on ears other than those used to protect hearing or communicate company business.

Construction access to and from the work area shall only be by Port-approved escort.

Use a guide person when it is necessary to back vehicles out of work areas within the airfield environment.

Confine parking, loading, and unloading of vehicles and equipment to within the work area.

Construction equipment that extends 15 feet or more above ground level shall be cleared through the Port prior to moving onto site.  Equipment that may be lowered readily shall be lowered at night, during reduced daytime visibility, and during other periods of storage to comply with the 15-foot height limitation.

If directed by the Port, construction equipment that cannot be lowered below the 15-foot height limitation shall be lighted at night and during periods of reduced daytime visibility.  Light shall be mounted on highest point of equipment; shall be omni-directional; and shall consist of, as a minimum, one 100-watt bulb enclosed within an aviation red lens.  Also, for daytime operations, mount an FAA-approved three-foot square orange and white checkered flag at the high point.

Place barricades or stakes around perimeters of work areas.   Barricade design shall conform to specifications of Manual on Uniform Traffic Control Devices for Type II barricade as a minimum.  Mount flashers on barricades and keep visible and operating at all times.  Flashers shall conform to Type A omni-directional barricade warning lights specifications in the cited manual.  Work area limits shall be staked with 3-foot stakes at 50-foot intervals in areas of dirt or grass.  Barricades or cones used to delineate work area limits on paved surfaces shall be spaced a maximum of 25 feet apart, or as specifically described for each work area.  Firmly anchor or weight barricades as required.  Additional barricades shall be kept in the staging area to be placed around the project area as directed by the Port or Airport Operations Staff.

All radio communication with FAA Ground Control will be coordinated through Airport Operations personnel.

Ensure that the airfield environment is kept continuously free of construction debris, equipment, and/or materials that might endanger or be ingested by an aircraft.

For emergency purposes, all escort vehicles shall be equipped with radio, telephone, or similar device for contact by Port or Airport Operations personnel.  In the event of an emergency, be prepared to move workers, vehicles, and equipment immediately at the direction of the Port.

Report emergencies to the Port and to 911.

When cranes are used, the following requirements shall be met:

An FAA-approved, 3-foot orange and white checkered flag and a solid red light shall be mounted at the highest point on the crane.

During daylight hours with severe visibility problems or heavy fog, cranes shall not operate.

The Port will determine when visibility problems exist and will coordinate and designate requirements for position and location of flag and light.

REMEDIES OF THE PORT UPON VIOLATION OF REGULATIONS REFERENCED OR CONTAINED IN THIS SECTION

In addition to any other rights or remedies that the Port may have in the event that the Contractor, subcontractor, anyone directly or indirectly employed by any of them, and anyone for whose acts any of them may be liable fails to comply with the regulations referenced or contained in this section, the Port shall have the right to:

Suspend the work or any portion thereof and continue the suspension until completion of any investigation or evaluation by the Port and full compliance with any corrective measures which the Port may reasonably require.

Require the Contractor to provide to the Port a written plan, satisfactory to the Port, to demonstrate the Contractor’s ability to prevent future violations.

END OF SECTION 013513