This master should be used by designers working on Port of Portland construction projects and by designers working for PDX tenants (“Tenants”).  Usage notes highlight a few specific editing choices, however the entire section should be evaluated and edited to fit specific project needs.

SECTION 101453 – TRAFFIC SIGNAGE

GENERAL

DESCRIPTION

This section includes furnishing and installing permanent traffic signs and temporary traffic control.

REFERENCES

ODOT:  Oregon Department of Transportation – Standard Specifications

ODOT Section 00910: Wood Sign Posts

OSSC:  Oregon Structural Specialty Code

USDT:  U.S. Department of Transportation, Manual on Uniform Traffic Control Devices

PRODUCTS

SIGNS

Conform to the USDT Manual on Uniform Traffic Control Devices and as shown on the drawings.

“Exit Only” shall be Rainbow Signs OIND193, or equal.

“Dead End” and “Stop” shall be Rainbow Signs OIND070, or equal.

ADA accessible signage shall be in accordance with OSSC.

POSTS

Conform to ODOT Section 00910 and as shown on the drawings.

FASTENERS

Lag bolts shall be galvanized.

Washers shall be stainless steel with neoprene.

CONCRETE

See Section 033000, Cast-in-Place Concrete, for Class.

EXECUTION

PERMANENT SIGN INSTALLATION

Locate and erect as shown on the drawings or as designated by the Port.

Space the “No Parking” signs approximately 500 feet apart on each side of the road or as directed.

TEMPORARY TRAFFIC CONTROL

One lane of traffic shall be open at all times.

GUARD RAIL

Relocate as shown on the drawings.

END OF SECTION 101453